## Slide 1: Adaptive Piecewise Multilinear Maps for Robust, Generalizable Data-driven Turbulence Models CSE 598-002 Final Project
Computational AeroSciences Laboratory
Department of Aerospace Engineering, University of Michigan
Ann Arbor, MI, USA
Niloy Gupta

## Slide 2: Generalizable Turbulence Models
Extract information from systems X1, X2,.. Xn, and make predictions in different systems Y, Z that share similar physics
Generalizable ⇒ predictive capability on unseen configurations

## Slide 3: Ensuring Robustness
Typically, ML models use neural networks
  Excellent approximators
  Drawbacks
    Poor extrapolators
    Many design and training options
    Expensive to train
Answer: localized learning
  ML model should only deviate from baseline in regions with data
  At worst, ML model predicts baseline behavior
  Ensures physically realizable predictions
How can we ensure robustness during extrapolation?

## Slide 4: Piecewise Multilinear Maps (PMMs)
Discretize feature-space
Model parameters are desired output values
Parameters only change if data is nearby
  Intrinsically implements localized learning
Uniform discretization
  PMM structure is implicitly stored
  Constant-time complexity output calculation
  Simple implementation
Shown to outperform neural networks
  Easier to train
  Consistent, robust extrapolative behavior
  Improved generalizability

## Slide 5: Issues with Uniform Discretization
Calculations in red cell always return baseline model
In same region, calculations influenced by training data

## Slide 6: Adaptive PMM Implementation
Take inspiration from pointwise adaptive mesh refinement
  Hyperoctree refinement of cells
  Keeps a structured representation
  In regions with more data, have smaller cells
  Ensure neighboring cells do not vary by more than a factor of two
Developed a simple n-dimensional mesh format
  Store which cells in each level are refined
  Store which nodes define or lie on every cell
PMM output calculation algorithm
  Input: feature coordinates
  Determine which leaf cell coordinates lie in
  If cell has no hanging node, use n-linear interpolation
  If cell has hanging nodes, use inverse distance weighting
  Output – Interpolated function value at feature-coordinates

## Slide 7: Application to Hypersonic Heat Flux
Problem: Standard eddy viscosity models fail to accurately predict heat transfer in
  Hypersonic boundary layers
  Shockwave-boundary layer interactions (SBLIs)
Goal: Improve post-interaction heat flux predictions
Possible cause: Constant turbulent Prandtl Number () in RANS energy equation
Augmentation: everywhere
Objective function:
  Mean-squared error of wall heat flux predictions wrt experimental data
Will compare to results from Gupta and Duraisamy (2026)
NASA, (2009)

## Slide 8: Model Design
Same input features as Gupta and Duraisamy (2026)
Feature 1 – turbulent to laminar viscosity
  ,
Feature 2 – wall-normal temperature gradient
  ⇒ trial-and-error of constants
Solve: s.t.
  0
Feature | Lower Bound | Upper Bound | # Nodes Level 0
 | -4.0 | 4.0 | 6
 | -1.5 | 1.5 | 6
Feature | Lower Bound | Upper Bound | # Nodes Level 0
 | -4.0 | 4.0 | 6
 | -1.5 | 1.5 | 6

## Slide 9: New Feature Space Discretization
1681 parameters 261 parameters

## Slide 10: Cases and Data
Training: Schulein (2006)
Validation: Nicholson et al. (2024)
Mach 5
Flat plate
Oblique impinging shocks
S14 ⇒ 14° shock deflection angle
  Strongest shock, flow separation
Mach 5
Curved wall
Intrinsically generated shock

## Slide 11: Results
Adaptive PMM implementation works
Yields improved heat transfer predictions during training

## Slide 12: Results
My handcrafted adaptive mesh seems to be causing problems
  RANS simulations struggle to converge
  Inferred augmentation fields for adaptive PMM miss some features the uniform PMM learned
Uniform
Adaptive

## Slide 13: Conclusions
Integrated an adaptive PMM within a RANS solver
  Significantly reduce number of parameters in the model
  Yielded improved predictions during training
  Adaptive mesh is inadequate
Future work
  Improve the adaptive mesh used
  Develop framework for automatic adaptive PMM mesh generation
  Extend adaptive PMM implementation to n-dimensions
  Improve quadtree mesh memory usage and search algorithm

## Slide 14: Appendix

## Slide 15: Model Consistent Learning
Learn directly ⇒ Consistent modeling ⇒ Improved accuracy
High-fidelity data ()
Model field data ()
Inference/learning
Model augmentation
Trained model
Prediction
Infer model environment and learn in the context of the model
Srivastava and Duraisamy, 2021
Notes: If we have a discrepancy model beta expressed in terms of features eta of model states u, we can embed this model into our fluid solver and perform an iterative optimization procedure. With this approach, we learn how to predict high fidelity data in terms of low fidelity states, ensure model consistent and improving accuracy.

## Slide 16: Model-embedded Inference
Start with |  | 
RANS solver | Baseline augmentation | Cost function
Start with |  | 
RANS solver | Baseline augmentation | Cost function
Goal
s.t.
Sensitivities ⇒ iteratively update
Backpropagation or computational tapes ⇒
Adjoint computation ⇒
Solve ⇒
Chain rule ⇒

## Slide 17: Learning Framework
Generalizability to unseen configurations
Physics-informed feature selection
How to introduce ?
Inference from limited data
Parsimonious set of features
Physics-based non-dimensionalization
Appropriate bounded functional form
Minimized spurious predictions
Localized learning
One-to-one feature-to-augmentation map
Srivastava and Duraisamy, 2021
Learning and inference assisted by feature-space engineering
(LIFE)

## Slide 18: Generalizability of PMMs
Generalizability depends on number of parameters
Idealized Model
Inferred Augmentation ()
Returns to baseline away from training data

## Slide 19: Mesh File Format
Line 1 – Header
  Number of dimensions
  Number of cells in each dimension at coarsest level
  Number of refinements
Section 1 – Mesh tree
  -2 ⇒ Cell does not exist
  -1 ⇒ Cell is refined
  0 ⇒ Leaf cell
Section 2 – Cell-to-node
  First numbers – vertices
  Remaining
    -1 ⇒ No hanging node
    0 ⇒ Hanging node

## Slide 20: Full PMM Output Algorithm